## Slide 1: Autonomous Predictive Tracking and Laser Neutralization System for Flies
Code: 26-1-R-22
  By:
Daniel Lachmakov | Daniel.lachmakov@e.braude.ac.il
Yaniv Bodaga | Yaniv.bodaga@e.braude.ac.il
Advsors:
Dr. Dan Lemberg | Lembergdan@braude.ac.il
Mrs. Elena Kremer | Elenak@braude.ac.il

## Slide 2: The Problem & The Need
The Issue: Flies cause contamination and disease transmission in homes, hospitals, and food industries.
The Challenge: Flies exhibit chaotic, rapid, and non-linear flight.
Current Solutions:
  Chemical sprays (Health risks, environmental damage).
  Manual swatting (Inefficient).
  Existing automated systems (Too slow/Reactive).
The Need: An autonomous solution that operates continuously and safely without human intervention.

## Slide 3: Why Existing Tech Fails (The Gap)
The "Reactive" Limit: Traditional systems aim at the current position.
System Latency: Camera processing + Motor movement = Delay.
Result: By the time the laser fires, the fly has moved.
Our Conclusion: You cannot hit a fly by looking at where it is. You must know where it will be .

## Slide 4: Engineering & Research Challenges
Visual Perception Challenges:
  Small Object Detection: Flies occupy very few pixels and suffer from significant motion blur due to high speed .
  Cluttered Backgrounds: Dynamic lighting and textured surfaces make extraction difficult .
The "Chaos" Factor (Modeling):
  Non-Linear Motion: Flies do not follow smooth paths; they exhibit rapid acceleration and abrupt turns that break standard Kalman filters.
System Constraints:
  End-to-End Latency: The physical delay between sensing and actuation often exceeds the fly's reaction time.
  Real-Time Computation: Running heavy Transformer models on high-frame-rate video (815 FPS) requires optimization.

## Slide 5: Proposed Solution & Innovation
The Goal: Build a system that compensates for latency using Future Trajectory Prediction.
The Solution:
  Vision: Detect flies in real-time.
  Brain: A Transformer-based AI model to predict the trajectory.
  Action: Aim the laser at the future coordinate .
Key Innovation: Applying Transformer architecture to flies flight paths, allowing us to model irregular, non-linear movement.

## Slide 6: Process Flow
Receive Video Input
AI-Based Human Detection
Track Fly Across Frames
Disable Operation
(Safety Stop)
Human Detected?
Yes
No
Predict Future Fly Positions
(Transformer Model)
Build Motion Trajectory
Align Laser to
Predicted Position
Attempt Fly Neutralization
AI-Based Fly Detection
No
Yes
Fly Detected?

## Slide 7: Computer Vision (Detection)
Camera: Area-scan, 815 FPS(75mm lens).
Human Detection (Safety):
  Uses a pre-trained robust CNN-based detection.
  Challenge: Occlusion(partly hidden), variable poses, varying appearance.
Fly Detection:
  Method: CNN-based detection fine-tuned on a fly dataset.
  Challenge: Motion blur and small pixel area.

## Slide 8: System Architecture(TrajLearn)

## Slide 9: Transfer Learning from TrajLearn
Handles sequences of any object motion, including small fast-moving targets.
Pre-trained on large trajectory datasets, enabling efficient transfer learning.
Produces smooth, reliable predictions for highly erratic motion like flies.
Can be optimized for real-time inference in high-speed applications.

## Slide 10: Loss Function- Cross entropy

## Slide 11: Success Metrics
We evaluate the model's prediction accuracy using standard error metrics:
Mean Absolute Error (MAE): Measures the average magnitude of errors.
Mean Squared Error (MSE): Penalizes larger errors more severely.
Root Mean Squared Error (RMSE): Provides error in the original unit.